## Slide 1: Tai Lung RV32I Core
Chris Shakkour
Shahar Dror

## Slide 2: Background
RV [32, 64, 128] I, M, A, F, D, G, Q, L, C, B, J, T, P, V, N
The FE310-G002 includes a SiFive E31 RISC-V core, which is a high-performance single-issue in-order execution pipeline, with a peak sustainable execution rate of one instruction per clock cycle. The RISC-V core supports Machine mode only as well as the standard Multiply, Atomic, and Compressed RISC-V extensions (RV32IMAC).

## Slide 3: Road map
Kick-off
Sep-2021
RV32I
May-2022
Privileged Arch
CSR
Jun-2022
Extensions
M+F
Aug-2022
FPGA
Sep-2022

## Slide 4: Specs
Spec | Tai Lung | SiFive E31
ISA | RV32I | RV32I-MAC
Arch | 5 stage pipeline | 5-6 variable stages pipeline
Operation frequency | 100 [MHz] | 320 [MHz]
IPC – instruction per cycle | 0.76 (avg) | 1 (avg)
Forwarding mechanisim | Yes | Yes
Branch prediction | No | No
cache | no | 16Kb 2 way Icache
Power | ? | ?
Area | ? | ?

## Slide 5: Architecture
RV32I - In order execution - 5 stage pipeline

## Slide 6: Memory
Memory block | Size | Address Range | Access | Port | Endianness
I-mem | 16Kbytes | 0x0000-0x3FFF | Read only - executable | Single | Little
D-mem | 48Kbytes | 0x4000-0xFFFF | Read/Write – non executable | Single | Little

## Slide 7: Core

## Slide 8: Decode pipeline
The Decode state decoded the 32-bit instruction into the core control signals and change the Core state to execute the instruction.
ALU cntrol
Branch cntrol
Mem
cntrol
Write Back
PC
Instruction
Forwarded data
RegisterFile data
PC
Immediate

## Slide 9: Execution pipeline
The Execution state execute the operation based on the instruction, calculate address for Load/Store instructions or decided if a branch operation should be taken.
Forwarded data
RegisterFile data
Data hazard control
Immediate
PC
ALU cntrol
Branch cntrol
Branch resulat
ALU resulat

## Slide 10: Execution pipeline
The Execution main component is the Arithmetic Logic Unit (ALU)
which preforms the arithmetic operation for the desired instruction

## Slide 11: Data hazard
Data hazard can happen when new instruction need to use a data from a Register before the data is available in the register file
0x0 - addi x1, x0, 5​
0x4 - add x2, x1, x1​
0x8 - add x3, x1, x1​
0xC - NOP​

## Slide 12: Data hazard – Forwarding unit
x1
Old
x1

## Slide 13: Load hazard
0x0 - LW x1, 0(x2)​
0x4 - Add x3, x1,x1​
0x8 - NOP​
0xC - NOP
Load hazard can happen when new instruction need to use a data which loaded from the memory in the previous instruction
x1
Old
x1
Old/irrelevant value

## Slide 14: Load hazard
0x0 - LW x1, 0(x2)​
NOP
0x4 - Add x3, x1,x1​
0x8 - NOP​
Load hazard can happen when new instruction need to use a data which loaded from the memory in the previous instruction
0x0 - LW x1, 0(x2)​
NOP
0x4 - Add x3, x1,x1​

## Slide 15: Control hazard
0x0 – jump/Branch 0x10​
0x4 - Add x3, x1,x1​
0x8 - Add x4, x10, x10​
0xC - Add x5, x11, x11​
0x10 - Add x6, x12, x12
Load hazard can happen when we have a conditional branch instruction and we don’t know which instruction to fetch
0x0 - LW x1, 0(x2)​
NOP
0x4 - Add x3, x1,x1​

## Slide 16: Control hazard
0x0 – jump/Branch 0x10​
0x4 - Add x3, x1,x1​
0x8 - Add x4, x10, x10​
0xC - Add x5, x11, x11​
0x10 - Add x6, x12, x12
0x0 – jump/Branch 0x10​

## Slide 17: Control hazard
0x0 – jump/Branch 0x10
NOP​
0x4 - Add x3, x1,x1​
0x8 - Add x4, x10, x10​
0xC - Add x5, x11, x11​
0x10 - Add x6, x12, x12
0x0 – jump/Branch 0x10​
NOP
instruction
NOP

## Slide 18: Control hazard
0x0 – jump/Branch 0x10
NOP
NOP​
0x4 - Add x3, x1,x1​
0x8 - Add x4, x10, x10​
0xC - Add x5, x11, x11​
0x10 - Add x6, x12, x12
0x0 – jump/Branch 0x10​
NOP
NOP
Next Instruction

## Slide 19: Performance
Power ?
Area ?
Test | Instructions retired | Cycles | IPC | Description
Tower of Hanoi | 28198 | 37924 | 0.743 | N of disks = 10
Sudoku solver | 3533 | 4909 | 0.720 | Cube = 9x9
Fibonacci | 470725 | 645863 | 0.728 | Fib(20)
Binary search | 652 | 751 | 0.868 | N=200 elements

## Slide 20: Validation plan
FPGA deployment
Validation trackers
Performance trackers
Data memory image comparison
Design review
RTL simulations
System-level simulation
ISA simulations

## Slide 21: Demo

## Slide 22: Alternatives… RISC based Arch
Apple-IBM-Motorolla
Acorn RISC machines
1978
Atmell arduino
Analog Devices
2000
1981-Stanford
Playstation-2
Wave computing

## Slide 23: RISC-V in the press